## Slide 1
UNIVERSITI TEKNOLOGI MARA
MEM261 :
WORKSHOP PRACTICE II
CHAPTER 1
Workshop Safety Regulations
An introduction to safe practice, hazard control and emergency procedure in the mechanical engineering workshop.
MEM261 · Chapter 1 · Workshop Safety Regulations
1

## Slide 2
Chapter Outline
1
1.1 Introduction — the purpose and goals of workshop safety
2
1.2 General Workshop Safety Rules, incl.
1.2.1 rules for machines
3
1.3 Industrial Safety — key definitions and concepts
4
1.4 Occupational Hazard and Control, incl.
1.4.1 PPE
5
1.5 Fire Safety — extinguisher classification
6
1.6 Important Workshop Signage, and chapter summary
MEM261 · Chapter 1 · Workshop Safety Regulations
2

## Slide 3
OBJECTIVES & LEARNING OUTCOMES
By the end of this chapter, you will be able to:
01
Explain workshop safety
Acquire knowledge of the safety precautions required while working in the mechanical workshop.
02
Use protective wear
Select and correctly use personal protective equipment appropriate to the task at hand.
03
Classify safety equipment
Identify and understand workshop safety equipment, for example fire extinguishers.
MEM261 · Chapter 1 · Workshop Safety Regulations
3

## Slide 4
1.1 INTRODUCTION
Why Workshop Safety Matters
The need for safety underpins the general goals of engineering practice. Every rule in this chapter serves one of the aims below.
1
Reduce accidents
2
Control or eliminate hazards
3
Develop new methods and techniques to improve safety
4
Maximize returns on safety efforts
5
Maximize public confidence with respect to product and service safety
Engineering safety goals exist to protect people first, and equipment, product and reputation second.
Guiding principle
MEM261 · Chapter 1 · Workshop Safety Regulations
4

## Slide 5
1.2 GENERAL WORKSHOP SAFETY RULES
Basic Safety Rules
1.Before you can use equipment and machines, or attempt practical work in a workshop, you must understand these basic rules — they protect you and everyone around you.
1
Free access to workshop areas is restricted to authorised personnel only.
2
Follow instructions
Always listen carefully to the workshop supervisor (SIR/MADAM/DR) and follow their instructions.
MEM261 · Chapter 1 · Workshop Safety Regulations
5
Restricted access

## Slide 6
1.2 GENERAL WORKSHOP SAFETY RULES
Basic Safety Rules
2. Safety in a machine shop divided into two:
1
2
Prevents worker injury
One category of machine-shop safety practice: those that prevent injury to workers.
Prevents equipment damage
The other category: those practices that prevent damage to machines and equipment.
MEM261 · Chapter 1 · Workshop Safety Regulations
5

## Slide 7
1.2 GENERAL WORKSHOP SAFETY RULES
Before Entering the Workshop
1
Wear the required PPE
Students must arrive at each session on time, with proper dress code – Personal Protective Equipment :lab coat and shoes. Slippers are not allowed.
- it is your first line of defence.
2
Dress appropriately
Jewellery and loose clothing are prohibited. Long hair must be completely covered, and this applies especially to female students.
MEM261 · Chapter 1 · Workshop Safety Regulations
6
Basic Safety Rules:

## Slide 8
1.2 GENERAL WORKSHOP SAFETY RULES
Before Entering the Workshop
3
Enter the laboratory
Students are not allowed to enter the laboratory without permission from the lecturer, assistant lecturer, or assistant engineer, working alone or unsupervised in laboratories is forbidden.
.
4
Bags
Bags are not allowed in the laboratories.
MEM261 · Chapter 1 · Workshop Safety Regulations
6
Basic Safety Rules:

## Slide 9
1.2 GENERAL WORKSHOP SAFETY RULES
Rules of Conduct in the Workshop
3
Personal Protective Equipment (PPE) is provided and must be used wherever it is necessary.
MEM261 · Chapter 1 · Workshop Safety Regulations
7
5
Students are not allowed to eat, drink or smoke while working in the workshop
And are not allowed to run the machines with your hands wet.
4
Students are not allowed to run the machines when you are sleepy or under
medication.
1
Read the instructions carefully and follow the laboratory procedures.
Do not touch anything that you are not completely familiar with.
Familiarise yourself with all equipment and tools used in the workshop
before you begin work.
2

## Slide 10
1.2 GENERAL WORKSHOP SAFETY RULES
Rules of Conduct in the Workshop
MEM261 · Chapter 1 · Workshop Safety Regulations
7
8
Always be patient. Never rush in the workshop.
7
Do not run in the workshop — you could collide with another student and cause an accident.
6
Report any defective equipment to the workshop supervisor immediately.

## Slide 11
1.2 GENERAL WORKSHOP SAFETY RULES · CONTINUED
Housekeeping and Tool Care
1
Keep gangways clear, clean and neat before and after the workshop activities. Any oil spillage, grease, etc. must be cleaned up immediately.
2
Clean as you go. Tools and equipment must be cleaned.
Keep the work area clean of all materials except those needed for your work.
3
Return equipment. Precision measuring equipment, drills, etc. must be replaced in their cabinets after each working day.
4
Carry tools safely. When carrying tools, sharp edges should be pointed downwards.
MEM261 · Chapter 1 · Workshop Safety Regulations
8

## Slide 12
1.2 GENERAL WORKSHOP SAFETY RULES · CONTINUED
1
Tools and equipment
Tools and equipment must not be removed from the workshop without permission from the workshop supervisor.
2
Evacuate for fire
In the event of a fire, leave the building immediately and proceed to the assembly point.
3
Report everything
All unusual incidents — cuts, burns, direct chemical exposure — and emergencies must be reported to the supervisor, whether or not injury resulted.
MEM261 · Chapter 1 · Workshop Safety Regulations
9

## Slide 13
1.2.1 SAFETY RULES FOR MACHINES USED IN THE WORKSHOP
Operating Machines Safely
MEM261 · Chapter 1 · Workshop Safety Regulations
10
5
Use the appropriate machine for the work to be done.
2
When working with rotating spindles, jewellery and loose clothing are
prohibited, and long hair must be completely covered.
1
Read the Lab sheet procedure carefully and follow the safety and machining
procedures.
3
When learning how to use a machine, listen very carefully to all instructions
given by the workshop supervisor — ask questions if you do not fully
understand.
4
Ensure that you are circuit and equipment connections are correct before
turning “ON” the power supply.

## Slide 14
1.2.1 SAFETY RULES FOR MACHINES USED IN THE WORKSHOP
Operating Machines Safely
MEM261 · Chapter 1 · Workshop Safety Regulations
7
If a machine is fitted with guards, they must be used.
Equipment should never be used if the safety guards
have been removed.
6
No machine may be used, and no work undertaken,
unless the supervisor is satisfied that you are
capable of doing so safely.
8
Ensure that switches are “OFF”, the plugs are
unplugged, and the working area is cleaned before
you leave the workshop.

## Slide 15
1.3 INDUSTRIAL SAFETY
Key Definitions — Events
Accident
An undesired circumstance which gives rise to ill-health or injury, damage to property, plant, products or the environment, production losses, or increased liabilities.
Incident
Undesired circumstances and ‘near misses’ which could cause accidents.
Ill Health
Acute and chronic ill health caused by physical, chemical or biological agents, as well as adverse effects on mental health.
MEM261 · Chapter 1 · Workshop Safety Regulations
12
Core concepts and definitions that frame every safety discussion in this course.

## Slide 16
1.3 INDUSTRIAL SAFETY
Key Definitions — Hazard, Risk & Safety
Risk
The likelihood that a specified undesired event will occur, due to the realisation of a hazard by, or during, work activities or by the products and services those activities create.
Safety
The ‘control of accidental loss.’
MEM261 · Chapter 1 · Workshop Safety Regulations
13
Hazard
The potential to cause harm — including ill health and injury, damage to property, plant, products or the environment, production losses, or increased liabilities.

## Slide 17
1.3 INDUSTRIAL SAFETY · OSH CONCEPT
From Hazard to Accident: The OSH Chain
1
Hazard / Danger
Observable, or predicted from knowledge.
→
2
Risk
Not directly observable — the probability of harm to system elements being realised from exposure to hazard and danger.
→
3
Harm
Damage to system elements, whether long- or short-term.
→
4
Accident
Injuries, ill health, and damage.
MEM261 · Chapter 1 · Workshop Safety Regulations
14

## Slide 18
1.3 INDUSTRIAL SAFETY
Why Accidents Must Be Prevented
M
Moral / Humane
No one comes to work to be injured or killed.
C
Cost
Accidents cost organisations money — in downtime, retraining and replacement.
L
Legislation
Organisations carry a legal obligation to prevent workplace accidents.
Even a “near miss” hurts productivity
It costs time and money to retrain a new worker • new workers are initially less productive than experienced ones • goods or equipment lost must be replaced • other workers feel afraid or unhappy working somewhere that could injure or kill them — and this harms productivity.
MEM161 · Chapter 1 · Workshop Safety Regulations
15

## Slide 19
1.3 INDUSTRIAL SAFETY
Occupational Safety & Health Governance in Malaysia
Government of Malaysia
↓
Ministry of Human Resources
↓
Department of Occupational Safety and Health (DOSH)
NIOSH
National Institute of Occupational Safety and Health
OSHA
Occupational Safety and Health Act functions
MEM261 · Chapter 1 · Workshop Safety Regulations
16

## Slide 20
1.3 INDUSTRIAL SAFETY
The Role of DOSH
1
Standard setting
Standards on safety, health and welfare are reviewed, drafted and finalised from time to time, so they stay relevant to workplace conditions.
2
Policy study
Existing OSH policies are studied periodically to assess how well they meet their objectives, and revised where needed.
3
Drafting regulations
New regulations, codes of practice and guidelines are drafted and amended to help industry meet its obligations under the Act.
4
Enforcement
Enforcement activities protect the safety, health and welfare of workers under the Acts listed opposite.
Enforced under
• Occupational Safety and Health Act 1994 (Act 514)
• Factories and Machinery Act 1967 (Act 139)
• Petroleum (Safety Measures) Act 1984 (Act 302)
Enforcement activities by DOSH include:
Approval & authorization
Registration
iii. Certification
v. Inspection
Investigation
iv. Litigation
17
MEM261 · Chapter 1 · Workshop Safety Regulations

## Slide 21
1.3 INDUSTRIAL SAFETY
NIOSH — National Institute of Occupational Safety and Health
NIOSH supports Malaysia's OSH system through five core responsibilities:
1
Training
Delivering OSH training programmes across industry.
2
Examination
Administering competency and certification examinations.
3
Information services
Publishing and disseminating OSH information.
4
Research & development
Advancing OSH knowledge and practice.
5
C1onsultation
Advising organisations on OSH matters.
MEM261 · Chapter 1 · Workshop Safety Regulations
18

## Slide 22
1.3 INDUSTRIAL SAFETY
OSHA — Objectives, Scope & Application
Objectives
• Secure the safety, health and welfare of persons at work against risks arising from work activities.
• Protect persons at a place of work, other than those at work, against similar risks.
Scope
Covers all working personnel, except:
• Armed Forces
• Crew of merchant ships
Applies across industries including:
Manufacturing
Mining & Quarrying
Construction
Agriculture, Forestry & Fishing
Utilities
Wholesale & Retail Trade
Finance & Insurance
Transport, Storage & Communication
Hotels & Restaurants
Real Estate & Business Services
Public Service & Statutory Authorities
MEM261 · Chapter 1 · Workshop Safety Regulations
19

## Slide 23
1.4 OCCUPATIONAL HAZARD AND CONTROL
What Is a Hazard?
Hazard: a substance or condition with the potential to cause injury in a given environment or situation.
• Industrial hazards may be defined as any condition/ substance produced by industries that may cause injury or death to personnel or loss of product or property.
•Safety in simple terms means freedom from the occurrence of risk or injury or loss. Industrial safety refers to the protection of workers from the danger of industrial accidents.
•Hazard is a potential of substance to cause damage
Risk: the probability that harm will occur under defined conditions of exposure to a hazard.
•In some industrial plants, by the nature of their activities and the substances they use, constitute hazards which are all the greater when they are located close to residential areas and their residents are particularly exposed in the events for accidents.
MEM261 · Chapter 1 · Workshop Safety Regulations
22

## Slide 24
1.4 OCCUPATIONAL HAZARD AND CONTROL
Types of Industrial Hazards
1
Mechanical hazards (press machines and other machinery)
2
Electrical hazards
3
Safe use of lifts and escalators
4
Noise and vibration hazards
5
Radiation, pressurized environments and thermal stress
6
Transport activities and gas cylinder safety
7
Fire safety in buildings (Fire Services Act, Building Law)
8
Safety at construction sites
9
Chemical hazards and chemical safety management
MEM261 · Chapter 1 · Workshop Safety Regulations
21
Identifying industrial hazards, and the hierarchy of controls used to manage them.

## Slide 25
1.4 OCCUPATIONAL HAZARD AND CONTROL
What Is a Hazard?
Workplace hazards can come from a wide range of sources. General examples include any substance, material, process, practice, etc. that has the ability to cause harm or adverse health effect to a person under certain conditions. See Table 1
Workplace Hazard | Example of Hazard | Example of Harm Caused
Thing | Knife | Cut
Substance | Benzene | Leukemia
Material | Asbestos | Mesothelioma
Source of energy | Electricity | Shock, electrocution
Condition | Wet floor | Slips, falls
Process | Welding | Metal fume fever
Practice | Hard rock mining | Silicosis
MEM261 · Chapter 1 · Workshop Safety Regulations
22

## Slide 26
1.4 OCCUPATIONAL HAZARD AND CONTROL
Categories of Workplace Hazards
1
Physical
Noise, vibration, temperature, lighting
2
Chemical
Fumes, dust, corrosives, solvents
3
Biological
Bacteria, viruses, moulds
4
Ergonomic
Poor posture, repetitive strain, manual handling
5
Psychosocial
Stress, workload, bullying, long hours
6
Energy sources
Electricity, pressurised systems, radiation
7
Natural
Heat, flooding, extreme weather
8
Property & security
Theft, fire, unsafe premises
MEM261 · Chapter 1 · Workshop Safety Regulations
23

## Slide 27
1.4 OCCUPATIONAL HAZARD AND CONTROL
Identifying Hazards at the Workplace
1
Observe your workplace
2
Investigate complaints from workers
3
Examine accident and near-miss records
4
Examine sickness figures
5
Use simple surveys to ask co-workers about health and safety concerns
6
Use checklists to help inspect your workplace
7
Learn the results of inspections by the employer, the union, or anyone else
8
Read reports or other information about your workplace
MEM261 · Chapter 1 · Workshop Safety Regulations
24

## Slide 28
1.4 OCCUPATIONAL HAZARD AND CONTROL
Hierarchy of Controls
MEM261 · Chapter 1 · Workshop Safety Regulations
Elimination & Substitution
Most effective — requires a physical change to the workplace
Engineering Controls
Requires a physical change to the workplace
Administrative Controls
Requires the worker or employer to do something
Personal Protective Equipment
Least effective — requires the worker to wear something
Most effective
Least effective
25

## Slide 29
1.4 OCCUPATIONAL HAZARD AND CONTROL
Eliminate/Substitution & Engineering Controls
Elimination & Substitution
At the source of the hazard:
Elimination — Getting rid of a hazardous job, tool, process, machine or substance entirely — e.g., a business decides to stop buying and cutting up scrapped bulk fuel tanks.
Substitution — Sometimes doing the same work in a less hazardous way is possible — e.g., replacing a hazardous chemical with a less hazardous one.
Engineering Controls
Redesign
Rework jobs or processes to be made safer, e.g. easier to hold or lift.
Isolation
If a hazard cannot be eliminated, isolate it — e.g. store flammables away from work areas.
Automation
Use dangerous processes robotically, protecting workers from direct exposure.
Barriers
Guarding that prevents contact with moving parts or hazardous zones.
Absorption & dilution
Absorb energy released, or dilute a hazard, e.g. ventilation systems dilute toxic gases.
MEM261 · Chapter 1 · Workshop Safety Regulations
26

## Slide 30
Administrative Controls
Administrative Controls
1
Safe work procedures expected practices, periodically reviewed and refreshed.
2
Training & supervision appropriate supervision helps identify hazards and evaluate work practices.
3
Job rotation reduces the time each worker is exposed to a hazard.
4
Housekeeping cleaning, waste disposal and spill cleanup keep hazards contained.
5
Hygiene practices shower and change clothing where applicable, to avoid taking toxic hazards home.
MEM261 · Chapter 1 · Workshop Safety Regulations
27
1.4 OCCUPATIONAL HAZARD AND CONTROL

## Slide 31
1.4.1 PERSONAL PROTECTIVE EQUIPMENT (PPE)
PERSONAL PROTECTIVE EQUIPMENT (PPE)
MEM261 · Chapter 1 · Workshop Safety Regulations
PPE — the control of LAST RESORT
Purpose: to increase individual safety while performing a potentially hazardous task.
1
Eye protection
2
Hearing protection (mandatory above 85 dB for more than 8 hours)
3
Dust masks
4
Foot wear
5
Gloves
6
Laboratory coats
7
Body protection
27

## Slide 32
1.5 FIRE SAFETY
Fire Extinguisher Classification
Every workshop must be equipped with a fire extinguisher. When selecting the appropriate type, the class of combustible material present must be considered.
CLASS A
RED
Combustible materials such as wood, cloth, paper, rubber and many plastics.
CLASS B
LIGHT YELLOW
Flammable liquids and gases, oils, greases, tars, oil-based paints, lacquers, some plastics.
CLASS C
BLACK / GREEN
Class A and/or B materials in the presence of live electrical equipment, motors, switches and wires.
CLASS D
LIGHT BLUE
Combustible metals such as magnesium, titanium, sodium, potassium, zirconium and lithium.
MEM261 · Chapter 1 · Workshop Safety Regulations
28

## Slide 33
1.6 IMPORTANT WORKSHOP SIGNAGE
Reading Workshop Safety Signs
⊘
Prohibition
Red circle with diagonal bar — e.g. No Admittance, No Naked Flame.
●
Mandatory
Blue circle — e.g. Wear Safety Glasses, Wear Safety Boots.
▲
Warning
Yellow triangle — e.g. Danger, Keep Hands Clear of Moving Machinery.
■
Safe Condition
Green square — e.g. Fire Exit, First Aid Point, Assembly Point.
SAFETY FIRST · UTAMAKAN KESELAMATAN
MEM261 · Chapter 1 · Workshop Safety Regulations
29

## Slide 34
CHAPTER SUMMARY
What You Should Take Away
1
1.1 Workshop safety serves engineering's broader goals: fewer accidents, controlled hazards, and public confidence.
2
1.2 General and machine-specific rules protect workers and equipment — from PPE and dress code, to guards and permissions.
3
1.3 Accidents follow a chain: hazard → risk → harm → accident. Malaysia's OSH system (DOSH, NIOSH, OSHA) governs this.
4
1.4 Hazards are identified and managed through the hierarchy of controls — elimination first, PPE last.
5
1.5 & 1.6 Fire extinguishers are matched to material class; signage communicates hazard and instruction at a glance.
MEM261 · Chapter 1 · Workshop Safety Regulations
30

## Slide 35
REFERENCES
Sources Cited in This Chapter
1
Bawa, H. S. (1995). Workshop Technology. New Delhi: Tata McGraw-Hill.
2
Kalpakjian, S., & Schmid, S. R. (2010). Manufacturing Processes for Engineering Materials (6th ed.). Prentice Hall.
3
Farrah, N. (2013). Introduction to Bench Fitting [PDF document]. Retrieved from http://i-learn.uitm.edu.my/v2/
4
Rao, P. N. (2001). Manufacturing Technology: Foundry, Forming and Welding. New Delhi: Tata McGraw-Hill.
MEM261 · Chapter 1 · Workshop Safety Regulations
31